## Slide 1: Pet foods. Basic introduction.

## Slide 2: Petfoods – Understanding.
Food for pet animals living in close proximity with human
Dog food, cat food, aquarium and pond feeds, food for cage animals and birds
Pet animals have status of friend or family member with great sentimental value
Require nutritionally balanced diets
Sustaining an animals health over long period
Price is not most important criteria
Health aspect and subjective appearance to owner (buyer) is most important

## Slide 3: Pet foods vs. Packed RTE Foods.
41.00 CHF/kg
10.60 CHF/kg

## Slide 4: Cats and dogs, dentition.
Cats
distinct carnivore dentition
with large canines
and powerful carnassials
 hunting animal
 difficulties in balancing and grinding small, hard, round, dry petfoods
 prefere soft, chewy, meaty textures
Dogs
have carnassials and premolars
 hunting animal, omnivore preferences
 can chew and grind dry petfoods prior to ingestion
canines
carnassials
premolars
inscisors

## Slide 5: Nutritional requirements – Dogs.
Omnivorous, oportunistic carnivorous scavengers
50-100 times as many scent receptors as human
Convert proteins into energy and muscle
But are also able to convert carbohydrate into energy
Can tolerate prolonged starvation, can mobilize own fat reserves
Need less proteins than cats

## Slide 6: Petfoods – Dog food , nutritional declaration.
as advertised by European manufacturer 2007

## Slide 7: Nutritional requirements – Cats.
True obligate carnivore
10 times as many scent receptors as human
Needs animal protein to survive
need higher level of protein and fat to remain healthy
Require various meat derived nutrients
Starvation may lead to health disorder

## Slide 8: Petfoods – Cat foods, nutritional declaration.
as advertised by European manufacturer 2007

## Slide 9: Nutritional declaration in comparison.
as advertised by European manufacturer 2007

## Slide 10: Petfood typical ingredients.
Cereals and cereal by-products Whole cereals such as wheat, oat, corn or barley, wheat milling byproduct meals, broken rice, etc.
Meat and meat by-product meal, fish meal a large variety of byproducts from the meat and fish processing industry
Vegetable proteins Corn gluten meal, soy bean meal, sunflower press cake, wheat gluten, pea protein, etc.
Animal and vegetable oils Beef and poultry fats from animal rendering and from the vegetable oil industry, whole oil seeds, etc.
Functional ingredients Dietary fibers for bowel conditioning, humectants and sugars for regulation of water activity, mineral and organic acids for pH correction
Flavors and Colors Palatants such as hydrolyzed meat and meat byproducts, natural and synthetic food colors
Vitamins, probiotics and minerals Vitamin and mineral premixes, pre- and pro-biotics, enzymes, plant extracts, etc.

## Slide 11: Powder to kibble – dissolution of ingredients.
Main components
Cereals or cereal byproducts
Meat and meat by-products
Fine grinding and dissolution of macromolecules by thermo-mechanical extrusion process
Shaping and cutting into a specific shape upon expanding through die plate
Example
High fat chicken byproduct meal directly from rendering plant, containing sinews, bones, beaks, etc., fat content 20-25%.
Picture showing same raw material but mixed with whole cereal grains, ground and extruded into dry expanded petfood kibble.

## Slide 12: Overview Modules.
3. Preconditioning
4. Barrels
5. Screw elements
6. Cutter
7. Screw extraction
8. Heating / Cooling of Barrels
9. Steamdosing 10. Waterdosing
11. Control unit
1. Main features 2. Drive

## Slide 13: Preconditioning.
PolyTherm™
Compatible to:
  PolyTwin™
  PrioTwin™
Two stage design
Used with vertical stuffer
PrioTherm™
Compatible to:
  PolyTwin™
  PrioTwin™
One stage design
Mounted right on extruder inlet

## Slide 14: Cutter.
  More technical details:
  Sturdy and precise design for clean product cut and low wear on knives and die plates
  Cutting housing with hinged door for access to knives and cleaning
  Visual quality control
  Sample opening

## Slide 15: Cutter.
  Pneumatic-driven, lateral sliding, precisely aligned
  PolyTwin™ / PrioTwin™ / CompacTwin™ / EcoTwin™
  Knives adjustable during operation to keep constant product quality
  Quick change of knife head during extruder operation
  Quick die change
  International standards CE, GS, VUU
  Optional hot air flow through cutter box to prevent condensation.
  Customer benefits:
  Quick start-up
  Maximal production time, least down time
  Constant high product quality
  Easy to clean to keep sanitation
  Maximal productivity
  Automated operation
  Wide range of finished products
  Safe and secure operation

## Slide 16: Nutrition Product Portfolio – Extruder in the focus. Bühler’s Twin Screw Extruders.
PolyTwin™
PrioTwin™
CompacTwin™
EcoTwin™
Best Extruder
Lean Poly Twin
High Capacity
Perfor-mance Line

## Slide 17: Nutrition Product Portfolio – Extruder in the focus! Bühler’s Twin Screw Extruders. Alternativlayout
PolyTwin™
PrioTwin™
EcoTwin™
CompacTwin™
Best Extruder
Lean Poly Twin
Top Quality made in China
Aquafeed High Capacity

## Slide 18: Twin Screw Extruder Portfolio. Status Quo.
PiloTwin™
BCTM
Ø 30mm
BCTL
Ø 42mm
BCTG
Ø 62mm
BCTF
Ø 93mm
BCTH
Ø 125mm
BCTJ
Ø 175mm
PolyTwin™
PrioTwin™
EcoTwin™
for pilot plant applications / low throughput / high flexibility
polyvalent
flexible
lower functionality “prio” features only
adapted to Petfood / Aquafeed Industry (pressure / torque)
similar to PRIO but suitable for higher capacities
BCTM
Ø 30mm
BCTL
Ø 42mm
BCTG
Ø 62mm
BCTF
Ø 93mm
BCTH
Ø 125mm
BCTJ
Ø 175mm
CompacTwin™
Mid Market Extruder made in China

## Slide 19
Premium Pet foods.

## Slide 20: Multiple colored kibbles.
Consisting of:
  Low pressure dosing system for addition of color into venting section
Or alternatively:
  High pressure (piston type) dosing system for injection of color directly into working section
  Alternating color every 50-100s may yield a small percentage of mixed (impure) colors!

## Slide 21: Equipment for co-extruded petfoods (filled pillows).
Consisting of:
  Coextrusion die (2-fold, 4-fold, 6-fold)
  Filling mass dosing system (2-fold, 4-fold, 6-fold)
  Pillow crimper with feeding belt
 requiring ready made filling mass

## Slide 22: Equipment for semi-moist meat stripes.
Consisting of:
  Slot die with horizontal distribution
  Flash-off/ cooling belt
  Delayed cutting (guillotine type)
 due to special shape products require additional surface spraying and special handling device after cutting

## Slide 23: Premium pet foods – process steps.
Intake, batching, grinding
Mixing
Micro ingredients
Extrusion
Drying
Sifting, Grading
Packaging
Coating, cooling
Cooling, delayed cutting
Surface coating
Coex, twisting, etc.
Individual packaging

## Slide 24: Premium pet foods – manufacturing process.
Intake, batching, grinding, mixing
extrusion
drying
sifting, bagging
coating
cooling
cooling, delayed cutting
Co-extrusion
Liquids, meat, humectants, etc.

## Slide 25
Extrusion Peripherals –
Meat feeding equipment.

## Slide 26: Meat Preparation – State of the art in meat industry.

## Slide 27: Example – container dumping hoist.
Lifts and dumps full containers into pump hopper

## Slide 28: Meat feeding system.
  Meat ground to particles <2mm, must not contain long fibers or large chunks that can clog injection nozzles or flow meter orifice
  With large intake hoper allowing to add meat manually
  Eccentric screw pump with intake screw
  With additional agitator screw for improved intake
  With high level sensor for automatic refilling
  With safety grid at inlet
  Flow meter single tube, magnetic inductive with large orifice
  With recirculation tube for mixing of components and cleaning
  With large drain valve at bottom of pump

## Slide 29: Meat dosing system – example two step dosing.
  Large low pressure pump with large intake hopper and agitators at bottom
  Combined with high pressure dosing pump

## Slide 30
Extrusion Peripherals –
Slurry recycling system.

## Slide 31: Slurry recycling system.
Starting procedure
Wash water and slurry is collected in container. When cutter is closed the first product will sucked to cyclone and comes back to the sampling port
The operator measures makes ensures right density and pellet quality and switches bypass valve to dryer
In emergencies extruder controller may also switch gate to bypass triggering sonic alarm
Operator to solve problem and if product is ok, he switches gate manually back to the dryer
Operator will manually dump off-spec product to slurry tank
Maximum solids content is usually less than 20%. Fluctuation in solids content has minor impact on the extrusion process.

## Slide 32: Slurry system.
Features
Automatic water addition maintaining water level
Thermostatically controlled live steam addition maintaining temperature at preset value, usually approx. 80°C
High speed mixer homogenizing content
Access port for ease of maintenance and sampling
3-way valve allowing to recycle tank content or to drain content of tubes back into tank for pasteurization
Peristaltic dosing pump for ease of replacing pumping tube

## Slide 33: Slurry system – options.
Pneumatic shut-off valve at bottom of tank
Rotary piston pump instead of peristaltic pump for higher concentrations of slurry and for longer conveying distance
Pneumatic valves instead of manually operated 3-way valve for automatic recycling of slurry for preheating, draining or filling of tubes and for cleaning of line with steam
Gravimetric flow meter instead of magnetic inductive flow meter
Additional level sensor in middle of tank
5
1
2
3
4
grid
high level
fresh water
slurry to extruder
drains
low level
high speed mixer

## Slide 34: Engineering Customer Success.
www.buhlergroup.com