## Slide 1: Food Safety Nutrition.
Edyta Margas.
Innovations for a better world.

## Slide 2: Safety of low water activity foods has become new priority for the food industry and regulatory bodies.
Salmonella in dry food
New regulations &
Increased human health problems
Private standards
Janice Haney Carr, Centers for Disease Control and Prevention, USA
1 µm
Need of a validated kill step
Notes: Salmonella in dry foods:
Heat resistant
Can survive years in dry conditions
Small amount can cause illness
FSMA – proposed 2011, final rule accepted 2015, implemented by 2018

## Slide 3: Food safety hazard for extruded products.
Biological hazards:
Pathogenic bacteria* & viruses like Salmonella, Listeria, E. coli. Bacillus cereus, Norovirus, etc.
Pest like insects, rodents and birds.
Chemical hazards: edyta.margas@buhlergroup.com
Naturally formed toxins (e.g. mycotoxins from molds)
Undeclared allergens
Chemicals from the environment (e.g. pesticides)
Chemicals introduced in processing (e.g. lubricants)
Toxic compounds formed during processing (e.g. acrylamide*)
Intentional adulteration (e.g. banned additives like KBr)
Physical hazards:
Foreign material like glass, metal, plastic, wood, etc.
47% recalls in USA come from microbial contamination
Notes: pathogenic bacteria: means that the microorganism can infect or intoxicate humans or animals, in other words, the bacteria are harmful.
Acrylamide: Roasting of coffee, baking of cookies or frying of potato chips are processes where acrylamide may be formed. Acrylamide is considered a cancerogenic compound and industry has to apply mitigation strategies minimize the level of acrylamide. Reducing thermal impact, i.e. temperature, is the most effective method to reduce acrylamide formation.

## Slide 4: Outbreaks associated with cereals (WHO/FAO, 2015).
Cereal or Grain Product | Microbial hazard(s) | Cases | Country (year)
Toasted Oat Cereal | Salmonella Agona | 209 | United States (1998)
Puffed Rice Cereal | Salmonella Agona | 33 | United States (2008)
Infant Cereal | B. cereus | 2 | United Kingdom (2005)
 | Salmonella Senftenberg | 5 | United Kingdom (1995)
Cereal products plus rice and seeds/pulses/nuts | B. cereus | 46 | France (2011), France (2012), Switzerland (2012)
 | S. aureus | 11 | France (2009, 2011)
Bulgur | B. Cereus (temp. abuse) | 21 | Finland (2010), Denmark (2011)
Buckwheat | B. cereus | 52 | Poland (2009)
Flour (uncooked product) | Salmonella Typhimurium | 67 | New Zealand (2008)
 | E. coli O121 (frozen dough) | 35 | United States (2013)
Unspecified Grains | Salmonella Lika | 3 | United States (2003)
Rice Cake | E. coli (STEC) | 142 | Japan (2011)
Cooked Rice | B. Cereus (temp. abuse) | 382 | 
 | S. aureus | 52 | France (2001), Australia (2002), Portugal (2011)
 | C. perfringens | 23 | Australia (2005)
 | Salmonella Typhimurium | 2 | Australia (2010)
Cooked Pasta | B. cereus | 50 | Belgium (2004), US (2009), Germany (2012)
 | C. perfringens | 330 | Australia (2004), US (2004, 2009, 2010)
 | Salmonella | 44 | Austria (2005), United States (1996, 2004)
 | S. aureus | 98 | France (1988), US (1995, 1999, 2008), Belgium (2009)
Rice Noodles | S. aureus | 3 | Australia (2010)

## Slide 5: News associated with contaminated breakfast cereals 2017. Bühler Food Safety Intelligence - Safefood.ai.

## Slide 6: Trend: “Feed goes food and food goes pharma”.
Closing the gap:
hygienic design
Inactivation processes
monitoring & validation

## Slide 7: Food Safety measures.
Implement
a trusted
microbial
kill step
Ensure
top hygiene
Safeguard raw material quality
Notes: Who would have thought 10 years ago, that bacteria like Salmonella could also become the game changer for the dry-plant based food.
Today we know, that Salmonella can be present and survive for years on dry nuts, cereals, soy, spices.
And food and feed manufacturer need to apply preventive measures to ensure that the Salmonella don’t slip though to end consumers.
The way to control Salmonella in ready-to-eat food processing is: safeguard the raw material quality, implement a trusted kill step, and ensure GMP with good hygiene,

## Slide 8: Food Safety concerns all actors along the value chain. Pressure to act builds up from the end product / consumer side.
farmers traders agro-food food retailers caterers consumers/
convertors processors society

## Slide 9
Bühler Food Safety Initiative.

## Slide 10: Our Food Safety mission.
Harness Science & Technology to enable safe food and feed processing across the food value chain.
Notes: Bühler enables
safe feed & food processing
with technologies & services
for good hygiene,
reliable decontamination
and full traceability
to build trust in the
grain-feed-food value chain.

## Slide 11: Bühler: Leading the food safety challenge.
Building credibility
1 µm
Building intelligence into processing for safety
Hygienic design of plant and machines
Know how, education and training
Notes: Salmonella in dry foods:
Heat resistant
Can survive years in dry conditions
Small amount can cause illness
FSMA – proposed 2011, final rule accepted 2015, implemented by 2018

## Slide 12: Food Safety Training.
> 2000 employees trained
719 extensive training
Notes: The main markets for ebeam / inactivation technologies are spices, almonds (nuts in general) and sesame seeds. Mostly in EU, USA and India. However, many other grains and seeds as well as other countries will eventually follow.
We will focus on the regions where food safety is on the top: EU and USA
USA and EU account for 80% of the worldwide export
The main exporter is India – larger variety
Tackling EU and USA will open up new markets (South Asia and South America)

## Slide 13: We leverage our collaborative innovation platform for Food Safety.
Scientific community.
Suppliers & Customers.
Employees.
Partners.
Bühler Innovation Board.
  4000 registered 2000 voted 50 trained Products in development

## Slide 14: Developing our portfolio to build sustainable value chains.
Equipment
Processes
Service
Hygienic Design
& Engineering
Fit for purpose
compliant
cost effective
Reducing
contamination
biological, chemical, physical
Traceability
Enablers for food Safety Management
HACCP
Traceability
Sampling
From
spare parts & engineering
over
consulting & training
to
process monitoring & control

## Slide 15
Bühler Solutions.

## Slide 16
Avoid fungal infection
Inhibit fungal growth
Remove contaminated fractions
Notes: So what is our solution? If we have a look at the value chain there are different steps and possibilities. The first thing is of course to avoid fungal infection, starting on field and harvest. Even if we follow good agricultural practice, we can´t influence the weather. Especially if there is hot and at the same time humid weather during germination and the flowering stage, the plants get probably infected. On field and harvest we as Bühler have not a real influence. But it starts at the grain reception facilities. Proper storage is very important to avoid fungal infection and also to inhibit fungal growth. Moreover drying is an important factor to stabilize the grain and to inhibit further fungal growth. However, there are sometimes already contaminated grains from the field so we have to remove the contaminated fractions through cleaning. And the earlier we do this intervention, the better, also to prevent cross-contamination and losses during storage. That means that the grain reception facilities are the first line of defense. In the mills that accurate cleaning is already quite common, but we have to bring the topic up-stream. I am convinced that the necessary pressure from the consumer towards the grain facilities will increase in the coming years. Before I will explain you how that kind of cleaning works, let me say some words to the topic of monitoring. Up to now it is not yet marked as Bühler solution. However this is a major chance for us to develop IoT solutions and to offer IoT services like real-time analysis, detection and monitoring of mycotoxins.

## Slide 17: Consistent reduction of mycotoxin levels as early as possible. Efficient cleaning technologies at grain reception.
  Size separation: Coarse and / or small & broken kernels
  Aspiration: Dust & Husks
  Density separation: Shriveled kernels
  Optical sorting: Visual fungal signatures
  Combination of sieving machines with inlet and outlet aspiration GrainPlus / TAS
  Gravity separator Concentrator MTCB
  Optical sorting machine Sortex
Mycotoxin level
Notes: So this is still future, but what we can already offer is the grain cleaning work. You have to know that only a small fraction carries most of the mycotoxins. That helps us to remove these highly contaminated fractions through the combination of mechanical and density cleaning, aspiration and optical sorting. So first of all we have to use sieving machines like the GrainPlus or TAS machine to clean out coarse particles as well as small and broken kernels. Thanks to the integrated inlet and outlet aspiration we can also separate dust and light particles. That is truly necessary to reduce the mycotoxin levels because especially in the light particles and the broken kernels the concentration of mycotoxins is extremely high. If we talk about Aflatoxin reduction there is also a gravity separator like the concentrator MTCB important to get out shriveled kernels. Last but not least we always have to use an optical sorting machine to make sure that all contaminated kernels are out of the process. And here your customer can rely on the world leading optical sorting machine for grains in the field, the Bühler Sortex. So you can see here the issues of contaminated kernels on the left side and our solution on the right hand side that will help our customers to achieve a higher benefit.

## Slide 18: Bühler’s capabilities for foreign matter reduction.
Field & Harvest
Collection Point
Transport & Storage
Food & Feed Processing
Retail
Good Agricultural Practice
Pre-cleaning
Cleaning
Size separation
Aspiration
Density separation
Coarse cleaning
Separation
  Size separation (sieves and filtration)
  Aspiration (by air)
  Density separation (by liquids)
  Surface cleaning
  Metal Separation (magnets)
Optical Sorting
  Colour
  Near-infrared (InGaAs)
  Biochemical
  Laser
X-Ray
Manual detection and removal
Use of metal detectable plastics and rubbers
Good Manufacturing practice (hygienic design of equipment and facility, personnel hygiene policy, glass policy, pest control, bioterrorism policy, waste disposal, wood policy, factory cleaning procedures, sampling policy, best practices)
Manual inspection of integrity of a package

## Slide 19: We build knowledge on microbial reduction in processing. Example of wheat processing.
1’000’000
100’000
10’000
1’000
100
10
1
0.1
APC [CFU/g] (total No of microorganisms)
low ash flour
wheat
~ 1 log
dry cleaning
of wheat
~ 1 log
milling
(low ash
flour)
~ 2- 4 log
thermal treatment:
flour heat treatment;
cereal flaking;
Medium
water activity
(aw 0.65 – 0.85)
> 5 log
cooking process;
extrusion
High
water
activity
(aw > 0.95)
Some pathogenic microorganism like Salmonella are more heat resistant. Efficacy of Salmonella inactivation needs to be proven by validation.
bran
Typical microorganism load as
Aerobic Plate Count (APC) in wheat products
by physical separation
by thermal inactivation

## Slide 20: We develop new technologies for decontamination of dry foods. LEeB technology.
Low energy electron beam
Product presentation know-how
Gentle surface decontamination
e-
e-
e-
e-
e-
e-

## Slide 21: A complete hygienically designed extrusion plants is complex task.
Precon-ditioner
Extruder
Fluid Bed
Flaking Mill
TUBO Conveying
Dryer
Coating Drum
Toasting
Dosing
Raw Material Handling
Pneumatic Lines & Airlocks
Extrusion Addition Systems
Cyclones, Filters and Fans
Roller Mills
Hammer Mills
Sifters
Automation System

## Slide 22: Our portfolio only fulfills partly customer’s requirements regarding HD. Some good examples of hygienically designed products.
Stainless steel with food touching parts
Easy access for cleaning
Material certificates
Continuous weld
Kill-Step Validation
Notes: Boxes in the lower part of slides:
“What does hygienic machine design really mean? What do customers and regulators expect?”
Some examples

## Slide 23: Food Innovation Center.
Opened in May 2012
Designed as a Food Grade facility to accommodate:
  Customer’s trials,
  Provide training for customers and Bühler employees
  Demonstrate Bühler’s complete solution

## Slide 24: Bühler offers comprehensive Food Safety Support.
IoT service
Food Safety Consultancy
Monitoring, Reporting and
Corrective Actions
Food Safety Solutions
Validation of Extrusion Process
Extruder
Notes: Iot service – future, not yet implemented

## Slide 25: Extruder validation – microbial challenge studies.
Identification of specific pathogen of concern and surrogate
Inoculation of a raw material
Determination of log reduction needed
Introduction and recovery of inoculated material from the extruder
Determination of process conditions to be validated (worse case scenario: moisture, temperature, time, pressure, product etc.)
Validation at factory scale
Determination of critical control points
Verification and review

## Slide 26: Example process set up during validation.
Feeding of inoculated material
with safe pathogen’s surrogate
Known screw configuration
Pressure probe (Bars)
Feed rate measured (kg/h)
Drive speed (rpm)
Temperature probes (ºC)
Kg/h
Total throughput measured (kg/h)
Barrel pressure probe (Bars)

## Slide 27: Bread crumbs trials. Example results.
Log10 reduction
>6.4 cfu/g
Trial Set Up
Name | Value | Unit
Feed Rate | 500 | Kg/h
Water | 0 | Kg/h
Screw Speed | 800 | Rpm
Motor Load | 41 | %
SME | 120 | Wh/kg
Barrel Pressure | 5 | Bar
Product Temp Barrel 2. | 154 | °C
Die Block Temp. | 150 | °C
Die Block Pressure | 18 | Bar

## Slide 28: Future: IoT monitoring solution. Watching process with real time log kill calculations.
Report
Generate reports to identify trends, make improvements or complete audits
Monitor
Critical process parameters are monitored continuously
Adjust
Make adjustments to extrusion process quickly
Alert
Receive alerts when parameters are not being met
Store
Store production data automatically stored in a secure cloud location
Visualize
View real time production data on any web connected device
Extrusion Process
Safe Food

## Slide 29: Avoidance of cross-contamination after the kill step.
Intake raw material & storage
Dry mixing of ingredients
Extrusion
Flaking
Bagging
Conditioning
Toasting & cooling
KILL STEP
SAFE
UNSAFE
High hygiene zone
Hygienic plant layout

## Slide 30: Zone segregation – division between high and medium zone.

## Slide 31: Food Safety starts with a hygienic layout of the factory.
basic hygiene zone
medium hygiene zone
raw material
food ingredients
high hygiene zone
Ready-to-eat foods
Factory zoning

## Slide 32: Hygienically designed equipment portfolio.
Inline check sieve MKZI
Microdosing with top precision & hygiene, MSDF
Sanimix batch mixer
TUBEX MSDN
PolyFlakeTM
Ceres, ready-to-eat cereals dryer

## Slide 33: We are leading the way in hygienic design for dry processing industry and develop internal standards.
Bühler’s 10 steps to hygienic design
Understand processing purpose
Understand cleaning requirements
Define hygiene level
Understand relevant food safety hazards
Follow relevant industry regulations and hygienic design guidelines
Select construction material: fit for purpose & compliant
Design: solve the multi-requirement equation
Define manufacturing specification
Define installation requirements
Provide the documentation

## Slide 34
Automation Solutions.

## Slide 35: Protect your food production and increase the process quality.
Challenges for the food industry
Drying / Roasting
Validation Service
Intake
Product identification
Food Safety.
Extruder
Machine Control
Hygienic Design Cabling
Logistic
&
Traceability
Maintenance ProPlant
Plant control Functions
Notes: GAutNavFood

## Slide 36: Automation. The key enabler for food safety.
Risk Reduction
Operation
Log
  Data logging minimizes paper work – Easier data management
  Due diligence documentation
  Traceability functionality builds transparency in the value chain – Knowing the content of every batch
  User management for authentication and logging of operation activities – Traceability of operation
  Control and monitoring of bacteria kill steps (and other critical steps) - Product recalls are cost intensive
Data
Logging
Trace-ability

## Slide 37: Operational Historian. Full transparency of production.
Benefits
Support of quality officers to be compliant with norms and regulations.
Full transparency about the production in the past.
Less paperwork required because reports are generated computer based.
Function
Powerful SQL database for a long-term saving of production data.
Values for quality assurance and food safety are recorded and documented.
Displayed errors and messages as well as user interactions are archived.
Batch related reports enable transparency of the production.
Visualization of historical or current data with configurable trend charts.
Audit log
What
Who
When
Why
Previous value
Notes: Additional Information
With the long term history, trends, reports etc. can also be generated for data in the past.
Other systems in the market deliver only trends and reports for the actual production, or need an interface to a separate system.

## Slide 38: Traceability and Logistic. WinCos® logistic & trace modules.
    Is product transparency ensured?
    Which components are really in the finished product?
    All components and products are tracked.
    Products and components can be traced forward or backwards.
    Management of product lots brings deeper transparency.
    Warehouse management tracks bound products (bags or pallets) from I-Point until distribution point.
Challenge
Answer of Bühler

## Slide 39: Automation solutions: Traceability. Proof of traceability along the entire supply chain.
Benefit
Ensure products transparency with the exact content of finished products until the single ingredient component lot.
Food safety related production issues are transparent
Be sure the right ingredient components are added.
Function
Holistic and user friendly overview of incoming to outgoing goods and vice versa.
All process steps are completely registered and saved in a central database
Traceability of the product lots in the silo layers.
Audit log of each user interaction
Bar code identification verifies the right ingredient components of the production
Audit log
Notes: Additional Information
Product Traceability
Continous and user friendly overview from delivery back to receivals
All process steps completely registered and saved in a centralized database
Allows traceability view based on receivals, deliverys or production steps
Registering of silo layers
Registering of single product lots
Audit Log
Every user interaction is logged
Food safety related production issues are transparent
Effective filter function for fast localisation operation issues
Classification and description of operation issues
Identification systems
Bar code identification verifies the right ingredient components of the production
Labeling of bags or pallets enables product tracking in the warehouse with bar code identification
Batch related labeling of pre-weighed ingredients supports operators to add previous prepared hand additions to the corresponding batch
User authentication with RFID badge cards at operation stations

## Slide 40: WinCos® plant control (MES). Modules for data logging.
    Are all production batches transparent?
    Bacteria have been killed demonstrable?
    Necessary parameter changes are documented and authorized?
    Every batch is recorded in a sustainable database.
    Batch trending with printable reports and adaptable trend charts.
    Logging of every user interaction - what, who, when, why, previous value.
    User authorization with scalable user management.
Challenge
Answer of Bühler

## Slide 41: WinCos® plant control (MES). Contamination prevention modules.
    Is the machinery clean and ready for the next production batch?
    Are quality topics aligned between production (WinCos®) and laboratory (LIMS)?
    WinCos® has a contamination control module that locks unwanted production.
    WinCos® allows an automatic synchronization of quality relevant data, since it interacts with external systems (ERP, LIMS). This results in an interlocked production if the components had been interlocked in the LIMS.
Challenge
Answer of Bühler
Notes: Quittirung von Reinigungsschritten (oder Frage Hände gewaschen?)
Operational Prerequisits (OPRQ)

## Slide 42: Hygienic Design. Minimization of deposits.
    Could the product be contaminated by electrical equipment or its deposits?
    Are all surfaces, which allow deposits well cleanable?
    Vertical installation with basket tray to avoid dust accumulation.
    Reduction of closed surfaces, as trucking systems and conduit installations, and focus on better cleanable installation methods, as field boxes (due to less cables).
    Touch screen control panels are easily cleaned
Challenge
Answer of Bühler

## Slide 43: Food Safety is part of our promise to engineer customer success.
ENGINEERING CUSTOMER SUCCESS.

## Slide 44: Engineering Customer Success.
www.buhlergoup.com